## Slide 1: Optimal Control Theory Parallel Parking with Collision Avoidance for Four-wheeled Vehicles
Honglu He, Yidong Fu | 04/22/2020

## Slide 2
Agenda
  Introduction
  Technical Background
  Optimization Problem
    Model & Focus
    Dynamics
    Approach
  Collision Detection & Avoidance
  Results
  Future Improvements

## Slide 3
Introduction
  Vehicular Automation
    Usage of Mechatronics, AI, and Multi-agent system
  Application
    Autopilot
    Navigation
    Automatic drive

## Slide 4
Technical Background
  Existing technologies for the parallel parking is limited
    Codes and programs are mostly simple simulation
    The main body of the vehicle collides into walls and objects
  Parallel parking is not an optimal problem
    Limited involvement in optimizing cost
    More involvement in trajectory planning

## Slide 5
Model & Focus
  Parallel parking
    Common and universal behavior of vehicles
    Part of the self-piloting of vehicles
  Four-wheeled Automobile Simulation
    Represented and simulated as a rectangle
    Vertices represent four wheels respectively

## Slide 6
Model & Focus
  Representation of a parking slot
Parameters that visualize a slot in a cartesian frame:
Behavior of vehicle:
Vehicle is moving in x direction
Perform parallel parking at the slot
Figure 1: Parking Slot Model [1]

## Slide 7
Model & Focus
  Representation of a vehicle
Visualization of a vehicle:
Figure 2: Vehicle Model [1]

## Slide 8
Dynamics
  Nonholonomic system
    3 degrees of freedom (DOF) overall
    2 instant DOF (not able to slide sideway)
    Modeled by 4 variables , , and
  Four-wheeled Automobile Simulation
    Calculating next position given current position and inputs
    Update state and co-state dynamics
    Update input variables by gradient descent method

## Slide 9
Approach
  Without any obstacle, the problem could be modeled as a Two Point Boundary Value Problem.
  , w=50
Figure 3: Results without collision avoidance [1]
Figure 4: Results without collision avoidance [2]

## Slide 10
Approach
  Or we can minimize the steps to get to the destination.
  where =1.1
Figure 5: Results without collision avoidance [3]

## Slide 11
Collision Detection
  From the result without “obstacles”, we can see the potential collision is at the bottom boundary and upper right corner.
  For the red line, we simply detect if the edge point of the vehicle falls below the line
Figure 6: Parking Slot Model [2]

## Slide 12
Collision Detection
  For the green corner, taken the fact that the vehicle is a convex object, when it doesn’t collide:
    + + >
Figure 3: Collision Model [1]
Visualization of a vehicle and surrounding:

## Slide 13
Collision Avoidance
  The first idea is to push the vehicle toward the normal direction of the collision configuration.
  Taking the step before collision as starting point, and the desired final location is 10 units away in the normal direction, this is again a Two Point Boundary Value problem:
  Where is current step, with 3 more steps to push the vehicle further from the collision point in direction

## Slide 14
Collision Avoidance
  The same idea applies to the bottom boundary, given 3 steps to adjust the vehicle upward
  +
  These two avoidance function are added within the gradient descent function of the main optimization function.

## Slide 15
Trajectory Optimization
  The second idea we came up with is to generate a path first, and then loop to fix the collision part until a collision free system is reached.
  The basic idea can be demonstrated by the following Pseudo code
Path Generated
While !collision:
    Check collision point
    Given 3 steps around the collision point, push the vehicle away
    Minimize the following trajectory toward (

## Slide 16
Results
Figure 6: Optimized results with collision avoidance. [1]

## Slide 17
Future Improvements
  Smaller slot – if a solution is possible
  Research on reverse parking
    Different physical models and dynamics
  Take more complex system into consideration
    Parking slot located at ramps
  Optimization variables can be much more complex in real cases
  Complex feedback system for a real automobiles

## Slide 18
Reference
[1] “Example: Parallel Parking,” ICLOCS2: A MATLAB Toolbox for Optimization Based Control - Example: Parallel Parking. [Online]. Available: http://www.ee.ic.ac.uk/ICLOCS/ExampleParallelParking.html. [Accessed: 22-Apr- 2020].